## Slide 1
Lab Book 2.0. Couplers
Student:Nadia Martí García

## Slide 2: Instructions General
SCRIPTS
From GitHub 
  Fork the repo: https://github.com/cccanvas-upv/pic-upv-lab2.git
  Clone the repo using VSCode
Run the Jupyter Notebook:
  COUPLERS_Student.ipynb
Cross-Sections to be studied:
h
(height)
w (width)
Core
Cladding
w (width)
MMI Body
Cladding
Multimode Interference (MMI) coupler
Directional coupler (DC)
Core
g
(gap)
h
(height)

## Slide 3
Directional coupler

## Slide 4: Learning outcome #1 – Directional coupler length and coupling coefficient Wavelength 1.5 µm – width 1.2 µm – gap 0.6 µm
Comment results (distance needed for a complete energy transfer between waveguides, distance needed for splitting power in half.. )
Observamos que a una distancia de L= Lpi obtenemos toda la potencia en la guía de arriba.
Para conseguir la mitad de la potencia en cada puerto L= Lpi/2
deep waveguide
Paste L/Lpi vs K plot here

## Slide 5: Learning outcome #2 – 2x2 Directional Coupler gap 0.6 - 1.6 µm (step 0.1 µm) – Wavelength 1.55 µm
Gap= 0.6 um Lpi= 94.02742605176876 µm
Gap= 0.7 um Lpi= 128.065673339184 µm
Gap= 0.8 um Lpi= 173.96389977139225 µm
Gap= 0.9 um Lpi= 235.77407047787594 µm
Gap= 1 um Lpi= 318.88415207666543 µm
Gap= 1.1 um Lpi= 430.54761007638376 µm
Gap= 1.2 um Lpi= 580.4293623072576 µm
Gap= 1.3 um Lpi= 781.3901391727065 µm
Gap= 1.4 um Lpi= 1050.478684859016 µm
Gap= 1.5 um Lpi= 1410.6607123685528 µm
Gap= 1.6 um Lpi= 1892.4674124101916 µm

## Slide 6
Comment results (Coupling relationship, Lpi, losses, … )

## Slide 7: Learning outcome #3 – Parallel uncoupled waveguides Wavelength 1.55 µm, width 1.0 µm, gap to be found for uncoupled wvgs
Hints:
All waveguides running in parallel are coupled somehow. Controlling the degree of coupling is key for those waveguides you don’t want coupling over certain level (i.e. uncoupled waveguides). Uncoupled waveguide definition, we will use K<0.01. Parallel waveguide length = 10 mm (typical length of a chip). Find minimum gap shallow / deep w=1.0µm wvl 1.55 µm.
deep waveguide
Paste vs gap for 10 mm wvgs to be uncoupled
shallow waveguide
Paste vs gap for 10 mm wvgs to be uncoupled

## Slide 8
Multimode Interferometer (MMI) Coupler

## Slide 9: Learning outcome #4 – 4.1 2x2 Multimode Interference Coupler Wavelength 1.55 µm, wMMI = 6.6 µm
Comment results (Coupling relationship, Lpi, losses, comparison with Directional Coupler… )
I/O waveguide width (um) | Excess Loss [dB] | Ratio over OUTs
6.6 | 0.4217 | ['0.5152', '0.4848']

## Slide 10: Learning outcome #4.2 – 2x2 Multimode Interference Coupler - Optimization Wavelength 1.55 µm, wMMI = 6.6 µm
Comment results
I/O waveguide width (um) | dy | dL | Excess Loss [dB] | Ratio over OUTs
6.6 | 0.05 | -0.3 | 0.3800 | ['0.5097', '0.4903']

## Slide 11: Learning outcome #4.3 – 2x2 Multimode Interference Coupler – Optimization (II) Wavelength 1.55 µm, wMMI = 6.6 µm
Comment results
I/O waveguide width (um) | dy | dL | Excess Loss [dB] | Ratio over OUTs
6.6 + 1.1 | 0.05 | -0.3 | 0.0027 | ['0.5084', '0.4916']

## Slide 12: Learning outcome #5.1 – 1x4 Multimode Interference Coupler Wavelength 1.55 µm, wMMI = 13.2 µm
Repeat all the design process for a 1x4 MMI Coupler.
I/O waveguide width (um) | Excess Loss [dB] | Ratio over OUTs
13.2 | 0.9430 | ['0.2432', '0.2568', '0.2567', '0.2433']

## Slide 13: Learning outcome #5.2 – 1x4 Multimode Interference Coupler Wavelength 1.55 µm, wMMI = 13.2 µm
Repeat all the design process for a 1x4 MMI Coupler.
I/O waveguide width (um) | dy | dL | Excess Loss [dB] | Ratio over OUTs
13.2 | 0.07 | -1.1 | 0.7777 | ['0.2481', '0.2520', '0.2519', '0.2481']

## Slide 14: Learning outcome #5.3 – 1x4 Multimode Interference Coupler Wavelength 1.55 µm, wMMI = 13.2 µm
Repeat all the design process for a 1x4 MMI Coupler.
I/O waveguide width (um) | dy | dL | Excess Loss [dB] | Ratio over OUTs
13.2 + 1.35 | 0.07 | -1.1 |  | 

## Slide 15: Extra #1 – Directional wavelength dependence Wavelengths from 1.5 to 1.7 µm, gap = 0.6 µm, width 1.0 µm
Comment results
slab = 150nm
deep waveguide
Paste vs wvl for TE and TM plot here
shallow waveguide
Paste vs wvl for TE and TM plot here

## Slide 16: Extra #2 – Directional coupler gap dependence Wavelength 1.55 µm, width 1.0 µm, gap 0.2-2.4 µm (step 0.2 µm)
Make conclusions and observations from your results
slab = 150nm
deep waveguide
Paste vs gap for TE and TM plot here
shallow waveguide
Paste vs gap for TE and TM plot here

## Slide 17: Extra #3 – MMI coupler wavelength dependence Wavelengths from 1.5 to 1.7 µm, wMMI = 6.6 µm
Comment results (Important. Compare with Directional Coupler)
slab = 150nm
deep waveguide
Paste vs wvl for TE and TM plot here
shallow waveguide
Paste vs wvl for TE and TM plot here

## Slide 18: Extra #4 – MMI coupler body width dependence Wavelength 1.55 µm, wMMI = 5-10 µm (steps 0.5 µm)
Polarization independent coupler: is there any point for which the MMI coupler can work identically for TE and TM? Answer yes / no and explain why?
slab = 150nm
deep waveguide
Paste vs width for TE and TM plot here
shallow waveguide
Paste vs width for TE and TM plot here

## Slide 19: Thank you